## Slide 1
NO.4 E/R VENT. FAN (REV)
Start → Run → Stop Sequence Guide
Based on schematic HI-2536-ME-SD1 (p.072) & HI-2536-ME-SD2 (p.073) Controller: LUXCO SMC-503H | Autotransformer reduced-voltage start | EOCR 51
Hyundai Heavy Industries · Shipboard Engine Room Ventilation Fan (Reversible)

## Slide 2
1. System Overview
Main components involved in start / run / stop
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
2 / 9
52
Main MCCB
3-phase power in (R, S, T)
88F / 88R
Direction Contactors
Forward (Supply) Reverse (Exhaust)
ATr + 6-1/6-2
Reduced-Voltage Start
Autotransformer 80% / 60% taps
19
Transition Timer
≈ 30 sec Start → Full voltage
51 EOCR
Overcurrent Relay
SET 3.27 A INV characteristic
SMC-503H
Motor Controller
Local/Remote F-R Lamps & alarms
4FX / 4RX
Run Feedback
Aux contacts back to SMC
88SH
Space Heater
ON when motor stopped (if enabled)

## Slide 3
2. Pre-Start Conditions (Ready to Start)
All must be OK before pressing SUPPLY or EXHAUST
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
3 / 9
1
MCCB 52 CLOSED
3-phase power available to starter panel
2
SOURCE lamp ON
SMC-503H has AC 220 V control power (S1–S2)
3
ABNORMAL lamp OFF
No fault latched; EOCR not tripped
4
HEATING may be ON
Normal if HEATER switch = ON and motor was stopped
5
Ammeter ≈ 0 A
Motor not running; contactors open
6
EOCR healthy
Not in TRIP; SET’G = 3.27 A (drawing value)
7
Direction clear
Wait until fan stopped mechanically before F↔R change
8
Start count OK
Max 3 consecutive starts; then wait 40 min (ATr cool-down)

## Slide 4
3. Start Sequence — Overview (Supply / Forward)
Same logic for Exhaust / Reverse using 88R & 4RX
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
4 / 9
1
Press SUPPLY
Operator command
2
4F / SMC output
Run command to starter
3
88SH OFF
Heater drops out
4
Start 6-1 / 6-2
Reduced V via ATr
5
88F closes
Forward power path
6
Timer 19 ≈ 30 s
Transition wait
7
Full voltage
Run contactors transfer
8
4FX feedback
SMC confirms RUN
Expected indications after successful start (running)
• SOURCE = ON (white) • SUPPLY (or EXHAUST) RUN = ON (green) • ABNORMAL = OFF | INTERVAL = OFF | HEATING = OFF • Ammeter ≈ motor load (typical ~60–65 A near FLA 65.4 A) • EOCR measured current ≈ 3.0–3.3 A secondary (CT 100/5) under normal load

## Slide 5
4. Start Sequence — Detailed Steps
Power & control actions in order
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
5 / 9
A. Command
Operator presses SUPPLY (F) on SMC-503H (or remote F via GSP2). Internal 4F picks up. HEATING lamp goes OFF; 88SH drops.
B. Reduced-voltage start
Start contactors 6-1 / 6-2 close. Motor fed through autotransformer (ATr) at reduced voltage (80%/60% taps) to limit inrush. 88F (or 88R) path active.
C. Transition (Timer 19)
Timer 19 runs ≈ 30 seconds. After time-out, circuit transfers from reduced-voltage start to full-voltage run. 6-1/6-2 sequence completes.
D. Full-voltage run
Motor runs on full line voltage via 88F (Supply) or 88R (Exhaust). Interlocks prevent 88F and 88R both closed. Hour meter (HM) counts.
E. Feedback & protect
4FX (or 4RX) aux contact closes → SMC sees RUN feedback. EOCR 51 monitors CT current continuously (INV curve, D-TIME 6 s start delay).

## Slide 6
5. Running / Monitoring
What to watch while the fan is running
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
6 / 9
Door ammeter
~60–65 A typical FLA = 65.4 A
If rising toward/ above FLA → load issue
EOCR display
Measured A (sec.) SET’G = 3.27 A
If measured > SET’G → INV trip in minutes
SMC lamps
SOURCE + RUN ON ABNORMAL OFF
ABNORMAL ON = fault / overload path
Feedback
4FX / 4RX closed to SMC
Lost feedback may cause abnormal stop
EOCR 51 settings (from drawing)
Motor rating 65.4 A | Range 0.5–6 A | SET’G 3.27 A | O-TIME 10 s | D-TIME 6 s | CHA = INV | PF = OFF CT ratio (effective): 100/5 → secondary = primary ÷ 20 (example: 63 A primary ≈ 3.15 A on EOCR) Important: If EOCR measured > 3.27 while door meter looks normal, verify with clamp meter — EOCR may trip on INV delay.

## Slide 7
6. Normal Stop Sequence
Clean stop — no fault declared
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
7 / 9
1
Stop command
Press STOP on SMC or remote opens run command
2
4F / 4R drop
SMC releases forward/reverse output
3
88F / 88R open
Power contactors open; motor coasts down
4
Current → 0
Ammeter returns to 0 A
5
Heater ON
If HEATER = ON, 88SH closes; HEATING lamp ON
6
Final state
SOURCE ON ABNORMAL OFF RUN lamps OFF
Your observed after-stop state matched NORMAL STOP
SOURCE ON · ABNORMAL OFF · INTERVAL OFF · HEATING ON · Ammeter 0 A That means SMC released the run command (or control path opened as a “quiet” stop), not a declared abnormal trip. If unintended: check STOP contact, SMC seal-in (4F), remote GSP2.

## Slide 8
7. Normal Stop vs Abnormal Stop
How to tell what stopped the fan
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
8 / 9
NORMAL / COMMAND STOP
Lamps • ABNORMAL = OFF • HEATING = ON (if heater switch ON) • RUN lamps = OFF • INTERVAL = OFF Typical causes • STOP button pressed / intermittent NC • SMC 4F seal-in dropped • Remote run contact opened (GSP2) • Control power blip (may not latch abnormal) 88F replacement usually does NOT fix this
ABNORMAL / PROTECTION STOP
Lamps • ABNORMAL = ON (red) • EOCR may show TRIP / OL • RUN lamps = OFF • HEATING may still come ON after stop Typical causes • EOCR 51 trip (INV — can take minutes) • Overload / high current • Power fail path • Lost start/run feedback (4FX) after T1 Check EOCR trip state + clamp current before raising SET’G

## Slide 9
8. Quick Troubleshooting Flow (Stops After Several Minutes)
Use after-stop lamps + current readings together
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Hyundai Heavy Industries
9 / 9
Fan stops after several minutes — check lamps at the moment of stop
ABNORMAL ON?
Yes → EOCR / protect Check EOCR TRIP, clamp A
ABNORMAL OFF?
Yes → Command stop path STOP / SMC 4F / Remote
EOCR measured > 3.27?
Even if door amp ~63 A Verify with clamp meter
SUPPLY lamp off first?
Yes = SMC dropped command No = power side after SMC
Clamp ≈ EOCR (high)
Real overload / mechanical load Do not only raise SET’G
Clamp ≈ door (~63), EOCR high
False EOCR/CT reading Check CT & EOCR device

## Slide 10
9. Your Field Readings (as found)
Filled from panel checks during troubleshooting
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Field readings included
10 / 11
After-stop lamps
SOURCE ON · ABNORMAL OFF · INTERVAL OFF · HEATING ON
Matches NORMAL / command stop state
Door ammeter (running)
~ 63 A (FLA 65.4 A)
Under FLA — looks normal
EOCR measured
3.7 A secondary
Above SET’G 3.27 A — INV may trip in minutes
EOCR setting (drawing)
SET’G 3.27 A · CHA INV · D-TIME 6 s
Expected secondary at FLA ≈ 3.27 A (CT 100/5)
88F contactor
Already renewed
Did not cure delayed stop
Lamp test
All indicators OK
ABNORMAL lamp is good — so OFF means truly no alarm
Conflict to resolve
Door ~63 A vs EOCR 3.7 A
Use clamp meter on all 3 phases to decide real vs false

## Slide 11
10. One-Page Flowchart (print companion)
Same content as the A4 landscape PDF — keep beside the panel
NO.4 E/R VENT. FAN (REV) | HI-2536-ME-SD1/SD2 | Field readings included
11 / 11
START → RUN
1. Pre-start OK (52, SOURCE, no abnormal) 2. Press SUPPLY or EXHAUST 3. Heater OFF (88SH open) 4. Reduced V start (6-1/6-2 + ATr) 5. Timer 19 ≈ 30 s transition 6. Full voltage via 88F / 88R 7. 4FX / 4RX feedback to SMC 8. Monitor A + EOCR + lamps
NORMAL STOP
STOP / command drop 4F/4R release 88F/88R open → Amp 0 HEATING ON (if heater ON) ABNORMAL stays OFF Your after-stop state matched this → check STOP / SMC / remote
NEXT ACTION
Clamp all 3 phases while running Compare to door A and EOCR 3.7 If clamp ≈ 63 A: EOCR/CT suspect If clamp high: real overload Watch stop: SUPPLY lamp first? Retest in LOCAL only